## Slide 2: TLS pre-master secret logging 🙂 The technique we’ll be using - the best by far
TLS pre-master secrets are used to derive session keys
  The server private key is only used to authenticate the key exchange
    With Perfect Forward Secrecy (PFS) cipher suites, which are now the norm
  SChannel in Windows isolates TLS pre-master secrets in LSA
    LSA is a protected process, but all secrets are conveniently in one place
  Other TLS stacks don’t isolate TLS pre-master secrets in LSA
    Many applications support the “SSLKEYLOGFILE” environment variable

## Slide 3: LSA secret extraction method references
lsass API hooking blog post reference
https://b.poc.fun/decrypting-schannel-tls-part-1/
PSDetour module (Detour in PowerShell)
https://github.com/jborean93/PSDetour
Original tls-keylogger.ps1 script from Jordan Borean
https://gist.github.com/jborean93/6c1f1b3130f2675f1618da56633eb1fa

## Slide 4: Application-level packet logging 😐 Your application sees the bytes, but can you read them?
Why not simply dump the bytes from your application?
  Manual inspection of hex dumps is a time-consuming task
It’s tricky to “cook” a Wireshark capture file properly
  You need to reconstruct TCP/IP headers with a fake client/server, etc.
  Wireshark dissectors get confused by missing TLS over TCP/3389, etc.

## Slide 5: Network MITM Proxy ☹️ Houston, we have a TLS token binding problem
CredSSP has built-in MITM protection
  CredSSP server public key echo step
  NTLM/Kerberos channel binding token (CBT)
    Also known as Extended Protection for Authentication (EPA)
RDP has pre-TLS traffic (X.224 negotiation)
  All the MITM and reverse proxying tools expect “clean” TLS

## Slide 6: Server RSA private key ☹️ The best TLS 1.1 had to offer. Move on, forget about it.
It used to be a thing – please don’t try to force TLS 1.1 or TLS 1.2 with Perfect Forward Secrecy (PFS) ciphers disabled, you’ll only end up breaking Windows Update instead.

## Slide 7: Summary of TLS decryption techniques
Technique | Description | Recommendation
TLS Pre-Master Secret Logging | Log TLS pre-master secrets into a text file (SSLKEYLOGFILE) | 🙂 Yes!
Application-level packet logging | Log decrypted packet bytes from the TLS client application | 😐 Maybe, in some cases
Network MITM proxy | Intercept, decrypt and re-encrypt TLS traffic using a different certificate | ☹️ Not really an option
Server RSA Private Key | Use server RSA private key to decrypt corresponding TLS traffic | ☹️ No longer viable

## Slide 8: GETTING STARTED with Live RDP decryption in Wireshark

## Slide 9: Getting Started - Prerequisites
RDP Server
Test Windows VM
RDP client
RDP (decrypted)
RDP (decrypted)
LSA extended protection needs to be disabled
  Don’t use a production device!
RDP connections to/from the test VM can be decrypted
Install Wireshark in the test VM for now (not your host)

## Slide 10: Hyper-V Lab (Optional)
  https://github.com/Devolutions/devolutions-labs
IT-HELP-RTR: Alpine Linux router with DHCP, NAT with host, etc.
IT-HELP-DC: domain controller with AD CS, root CA, HTTP CRL, etc.
IT-HELP-GW: RD Gateway, RDWeb, connection broker, licensing server
IT-HELP-WAC: Windows Admin Center

## Slide 11: Virtual machine bootstrapping
Disable LSA extended protection, then reboot:
Set-ItemProperty -Path 'HKLM:\SYSTEM\CurrentControlSet\Control\Lsa' -Name 'RunAsPPL' -Value 0
Install PowerShell 7 (yes, it's required):
iex "& { $(irm https://aka.ms/install-powershell.ps1) } -UseMSI –Quiet"
Set the PowerShell execution policy to Unrestricted:
Set-ExecutionPolicy Unrestricted -Scope LocalMachine

## Slide 12: Logging TLS secrets from LSA (SChannel)
Launch PowerShell 7 elevated, then install PSDetour:
Install-Module -Name PSDetour -Scope AllUsers –Force
Install the AwakeCoding.DebugTools PowerShell module:
Install-Module –Name AwakeCoding.DebugTools –Scope AllUsers –Force
Start logging TLS pre-master secrets, and leave terminal open:
Start-LsaTlsKeyLog

## Slide 13: Installing Wireshark
Using the installer
https://www.wireshark.org/download.html
Using chocolatey
choco install wireshark
Using winget
winget install WiresharkFoundation.Wireshark
Install Wireshark in the test virtual machine for now

## Slide 14: Configure Wireshark TLS Preferences
In Wireshark, open the Preferences dialog (Edit -> Preferences), navigate to the TLS section under Protocols, and then set the (Pre)-Master-Secret log filename to “C:\Windows\Temp\tls-lsa.log”

## Slide 15: Start Wireshark Packet Capture
In Wireshark, open the Capture Options dialog (Capture -> Options), select the correct network interface for RDP traffic (usually the one with active traffic that isn’t the loopback adapter) and then click Start

## Slide 16: Wireshark Live Decrypted RDP traffic
Use “tcp.port == 3389 or udp.port == 3389” as display filter, then launch mstsc and connect with RDP to the VM, you should see live decrypted RDP traffic in Wireshark:

## Slide 17: Related GitHub Repositories
Wireshark RDP resources
https://github.com/awakecoding/wireshark-rdp
AwakeCoding Debug Tools
https://github.com/awakecoding/AwakeCoding.DebugTools

## Slide 18: GOING FURTHER with RDP traffic decryption in Wireshark

## Slide 19: Going Further - Prerequisites
Client machine
RDP (decrypted)
TLS pre-master secrets
Install Wireshark on your client machine this time
We’re going to log TLS pre-master secrets remotely
Test Windows VM

## Slide 20: Logging TLS secrets remotely
In your test VM, start TLS key log server:
Start-TlsKeyLogServer -LogFile 'C:\Windows\Temp\tls-lsa.log' -Port 12345
-AllowInFirewall
On your host (or main device), start TLS key log client:
Install-Module AwakeCoding.DebugTools
Start-TlsKeyLogClient '10.10.0.25:12345' "$Env:Temp\tls-all.log"
In Wireshark, edit the TLS pre-master secrets file
You will now have TLS pre-master secrets extracted from the test VM streamed to your host, readily available for consumption in Wireshark

## Slide 21: Logging TLS secrets from multiple sources
In each test VM (logging source):
Start-LsaTlsKeyLog
Start-TlsKeyLogServer -AllowInFirewall
On your host (or main device):
Start-TlsKeyLogClient @('10.10.0.10', '10.10.0.25') "$Env:Temp\tls-all.log"

## Slide 22: Logging TLS secrets when not using SChannel
With FreeRDP:
Use the “/tls:secrets-file” command-line argument:
/tls:secrets-file:C:\Users\Public\tls-freerdp.log
With IronRDP:
Use the “SSLKEYLOGFILE” environment variable:
SSLKEYLOGFILE="C:\Users\Public\tls-ironrdp.log"

## Slide 23: Cleaning up RDP traffic for Wireshark
Disable RDP UDP transport
  Set-ItemProperty -Path 'HKLM:\SOFTWARE\Policies\Microsoft\Windows NT\Terminal Services\Client' -Name 'fClientDisableUDP' -Value 1
  DisableUDPTransport:i:0 (MsRdpEx only)
Disable bandwith auto-detection
  connection type:i:6
  networkautodetect:i:0
  bandwidthautodetect:i:0
Disable bulk data compression
  compression:i:0

## Slide 24: Injecting TLS secrets in capture file
In Wireshark: Edit -> Inject TLS Secrets
  This will embed TLS secrets inside the .pcapng file, so you no longer need the TLS key log file
  This is the best way to share decrypted packet captures – don’t send TLS key log files!
  You need to do this every time before exporting a capture file, it is not automatic
Alternatively, at the command-line:
  editcap.exe --inject-secrets “tls,tls-key.log” “input.pcapng” “output.pcapng”

## Slide 25: Exporting capture file
In Wireshark, File -> Export Specified Packets…
  Select “Displayed” to export with current packet filter
  Optionally select “Compress with gzip” to reduce file size

## Slide 26: Windows packet capturing methods
npcap
Default with Wireshark - supports live capturing, but silent installation (non-GUI) requires a special license
winpcap
Deprecated and unmaintained, but still mostly works
pktmon
built-in Windows command-line tool, it would be perfect if only it could do live capturing from Wireshark

## Slide 27: pktmon command-line capturing
Add capture filter
  pktmon filter add RdpFilter -p 3389
Start capturing
  pktmon start --capture --pkt-size 0 -f capture.etl
Stop capturing
  pktmon stop
Export .pcapng
  pktmon etl2pcap .\capture.etl -o capture.pcapng
Remove capture filter
  pktmon filter remove RdpFilter

## Slide 28: DEMO

## Slide 29: Sample Wireshark RDP capture files
https://github.com/awakecoding/wireshark-rdp

## Slide 38: QUESTIONS?

## Slide 39: Thank you! https://devolutions.net https://bsky.app/profile/devolutions.net https://awakecoding.com https://bsky.app/profile/awakecoding.com